## Slide 1
Connecting to the Rootbot
TL;DR;
Connect to Wifi network: RUT955_5D40, password = Gv31Uid2
Point browser to http://rootbot:8080/
Remember to turn the EM logger on (either in the mission plan, or manually) ...
Download data before powering down

## Slide 2
Pi5
Orange Cube
FC
EM
GPS1
GPS2
PyBoard
Router
Wifi
4G
Radio/Mavlink
Serial/USB
Ethernet
USB
I2C
Charging
(Victron)
BT
Components

## Slide 3
Charging unit ( victronenergy.com )

## Slide 4
Connect via WiFi RUT955_5D40, password = Gv31Uid2
Admin @ http://192.168.1.1
User admin
Pass d6Z7MsQu
pi companion ssh://192.168.1.126 (aka rootbot)
user qaafi
pass qaafi
Vpn (husarnet)
Router

## Slide 5
EM Monitor
Python app, starts at poweron. Assembles GPS & EM data to one frame.
Access through
WiFi: http://rootbot:8080/
VPN: http://[fc94:961e:1755:794e:f933:6ade:ac2:b7c1]:8080/
ssh: qaafi@rootbot (pass qaafi)
Browser can download data directly. Alternatively, use http://rootbot:8080/getData to download raw json (includes “unrecorded” data).
Recorded csv data is also in the qaafi home directory on the pi, accessible via ssh/scp.
App output (stdout, stderr) available from systemd
It’s a good idea to shutdown the device through the web page.
Source code
https://github.com/peter-devoil/EM-GPS-logger
Pi5
EM
GPS

## Slide 6
Motion
http://rootbot:8081/
Multiple cameras, recorded, 1f/s
Direct video stream (vlc, ..